01. What is a primary role of the Physical layer in transmitting data on the network?
a.  create the signals that represent the bits in each frame on to the media
b.  provide physical addressing to the devices
c.  determine the path packets take through the network
d.  control data access to the media

02. Which fiber connector supports full duplex Ethernet?
a.     






b.     







c.     







d.     








03. With the use of unshielded twisted-pair copper wire in a network, what causes crosstalk within the cable pairs?
a.  the magnetic field around the adjacent pairs of wire
b.  the use of braided wire to shield the adjacent wire pairs
c.  the reflection of the electrical wave back from the far end of the cable
d.  the collision caused by two nodes trying to use the media simultaneously

04. Which method of signal transmission uses radio waves to carry signals?
a.  electrical
b.  optical
c.  wireless
d.  acoustic

05. In LAN installations where potential electrical hazards or electromagnetic interference may be present, what type of media is recommended for backbone cabling?
a.  coax
b.  fiber
c.  Cat5e UTP
d.  Cat6 UTP
e.  STP

06. When is a straight-through cable used in a network?
a.  when connecting a router through the console port
b.  when connecting one switch to another switch
c.  when connecting a host to a switch
d.  when connecting a router to another router


07. Which characteristics describe fiber optic cable? (Choose two.)
a.  It is not affected by EMI or RFI
b.  Each pair of cables is wrapped in metallic foil
c.  It combines the technique of cancellation, shielding and twisting to protect data
d.  It has a maximum speed of 100 Mbps
e.  It is the most expensive type of LAN cabling

08. What are three measures of data transfer? (Choose three.)
a.  goodput
b.  frequency
c.  amplitude
d.  throughput
e.  crosstalk
f.  bandwidth

09. An installed fiber run can be checked for faults, integrity, and the performance of the media by using what device?
a.  light injector
b.  OTDR
c.  TDR
d.  multimeter

10. What characteristic of UTP cable helps reduce the effects of interference?
a.  the metal braiding in the shielding
b.  the reflective cladding around core
c.  the twisting of the wires in the cable
d.  the insulating material in the outer jacket

11. Which type of cable run is most often associated with fiber-optic cable?
a.  backbone cable
b.  horizontal cable
c.  patch cable
d.  work area cable

12. What is considered a benefit of wireless as a media choice?
a.  more host mobility
b.  lower security risks
c.  reduced susceptibility to interference
d.  less impact of the surroundings on the effective coverage area
13. Refer to the exhibit. Which type of Category 5 cable is used to make an Ethernet connection between Host A and Host B?

a.  coax cable
b.  rollover cable
c.  crossover cable
d.  straight-through cable

14. Which OSI layer is responsible for binary transmission, cable specification, and physical aspects of network communication?
a.  Presentation
b.  Transport
c.  Data Link
d.  Physical

15. In most business LANs, which connector is used with twisted-pair networking cable?
a.  BNC
b.  RJ-11
c.  RJ-45
d.  Type F

16. What is a possible effect of improperly applying a connector to a network cable?
a.  Data will be forwarded to the wrong node
b.  Data transmitted through that cable may experience signal loss
c.  An improper signaling method will be implemented for data transmitted on that cable
d.  The encoding method for data sent on that cable will change to compensate for the improper connection

17. XYZ Company is installing new cable runs on their data network. What two types of cable would most commonly be used for new runs? (Choose two.)
a.  coax
b.  Cat4 UTP
c.  Cat5 UTP
d.  Cat6 UTP
e.  STP

18. Which of the following is a characteristic of single-mode fiber-optic cable?
a.  generally uses LEDs as the light source
b.  relatively larger core with multiple light paths
c.  less expensive than multimode
d.  generally uses lasers as the light source